Quick Reference Guide

“Basic Key Operations”

|  | Disk operation: Load your design from USB or USB Floppy. |  |  | Speed Controls |  |
| --- | --- | --- | --- | --- | --- |
|  | Design Operation: Select design/ delete design. |  | Trim key | Manual Operation: Design trace | Exit/ Escape |
|  | Parameter Operation: Color change, design direction and rotation angle. |  | Preparation Mode | Embroidery Mode: (For high and low speed idling, refer to your manual.) |
|  | (Clear data Enter key( |  |  |  | Embroidery Confirmation Modes: Auto Color Change/Auto Start: In this mode, the machine will change and start the next color automatically. |
|  | Main Shaft Stop Position: When the light is OFF, the main shaft is NOT in position of (100). To set position, manually adjust the dial located on the RIGHT side of the machine back to 100. Quick TIP: Pressing the key will also RESTORE the position back. |  |  | Auto Color Change/Manual Start: This mode will change the color automatically and the operator manually starts the design each time. |
|  |  |  |  | Manual Color Change/ Manual Start: In this mode, the operator will manually change the colors and manually start the machine again. |
| The following keys do not have an everyday function. Please refer to your Manual. | Load to Embroidery in 6 STEPS. Load Design – Select “” Option 5 / Select Design. Orientation (P) “Use Arrows to Flip the Rotation.” Work Order (Option 9) Select Colors. In Preparation Mode, select “” Option 5 “Frame Range” and trace Design. Last Step – Set the Embroidery Mode “” |
| Origin Back: Return to Start Point. In preparation mode select “Origin Back” and press Machine “returns to start point” automatically. | Set Frame Origin: Follow these steps to set the Frame Origin for the Frame Restore function to work. From the MAIN MENU In preparation mode. Select the Assistant Function. Select Set Frame Origin, Option 5 Then Enter The following Screen will be displayed. Use UP/DOWN arrows to select YES/NO and press One “Set Frame Origin” is set; OPTION 2 “Frame Restore” is lit up. Follow these next steps to set the “Frame Restore.” Frame Restore: What to do when accidental power outage takes place. NOTE: Embroidery can continue if the frame/hoop has not been moved. From the MAIN MENU Select the Assistant Function. Select Frame Restore, Option 2 Then Enter The “Frame” will move first to the Origin Point and then to the Position where it was when the power shut off. |
| Delete Designs from Memory: Eternal memory can hold up to 99 designs. When this is FULL, you can remove one by one or ALL at the same time with the following steps. Delete One Design: In preparation mode. Press , then select Delete Design, Option 4 The following Screen will be displayed. Enter design number, and then press. Or Press Enter in this screen with out a number for the design directory. Once design is selected, press the. Delete ALL Designs: In preparation mode. Press , then select Delete Design, Option 8 The following Screen will be displayed. Chose Yes/No with UP/DOWN Arrows, and then Yes: Design memory has been deleted. |  |
| Trace Design: With directional ARROWS, set the Start Point. Main Menu/Preparation Mode Press the key, then Frame Range #5. Follow the Prompts on the Screen. | Machine Maintenance and Support 800-872-1555 |